## Slide 1: Interrupts vs. Polling

## Slide 2: Polling
Constantly reading a memory location, in order receive updates of an input value
while(1) {
key=IORD(KEY_BASE,0);
if( key == 0x02 )
{
//Do something interesting here
//Wait until no keys are pressed
while(IORD(KEY_BASE,0)!= 0x03)){}
}
}
Polling
Polling

## Slide 3: Interrupts
“Normal” microcontroller flow of control
  Single process
  Main routine / main loop
  Normal control flow statements (if, while, for, etc.)
Asynchronous, important events
  May need to be handled immediately
  Realtime requirements
  Interrupt normal flow of control

## Slide 4: Interrupt Handling
Processor interrupts (preempts) the current flow of control
Time spent in interrupt handlers should be kept as short as possible
Microcontroller offers interrupts for various conditions
  Not all are useful all the time: enable required interrupts
  Some critical may require atomic execution (no interruptions guaranteed)
  Disable / re-enable interrupts around critical section

## Slide 5: In details
Task execution
Task execution
Interrupt signal
ISR

## Slide 6: In details
Saving context: Push all temporary variables (like program counter) into stack
Task execution
Task execution
Interrupt signal
Saving context
ISR

## Slide 7: In details
Construct context: Pull all temporary variables (like program counter) out of stack
Task execution
Task execution
Interrupt signal
Saving context
ISR
Construct context

## Slide 8: Sources of Interrupts
Timers: System “ticks”, periodic tasks
Communications
  Ethernet
  USB
  Serial
Periphery
  E.g. ADC (Conversion complete)
  Memory management
Software
    Software interrupts (trap instructions) / illegal instructions
Reset / Power-On

## Slide 9: Interrupt Priorities
What happens if a interrupt occurs during another interrupt is handled?
  E.g. Timer ticks while Ethernet packet is processed
  Priorities: Some interrupts are more important than other
  Hierarchy of interrupts
    Only more important interrupts may preempt lesser interrupts
    Usually: lower priority is more important
    Interrupts on same priority level do not preempt
  Not immediately handled interrupts may be stored or may be lost
    Depends if interrupt condition persists

## Slide 10: Interrupt Latency
Latency
  Time passed between occurrence of event and handling
  Interrupt is generated and source is serviced
  Important measure for real-time applications
Interrupt latency
  Interrupts tightly integrated into processor
  Complete current instruction, save registers and jump to handler
Usually better latency with interrupts than with polling

## Slide 11: ISR
Event handler for interrupt is called Interrupt Service Routine (ISR) or sometimes callback function
Special, user-defined function for handling the interrupt (e.g reacting to some input)

## Slide 12: Trigger for external interrupts
Edge-triggered
  Falling Edge – when signal value decreases
  Rising Edge – when signal value increases
  Either Edge
Level-triggered
  each instance, when signal is above or below a certain threshold
IRQs can be configured from within SOPC Builder

## Slide 13: Interrupts vs. Polling
Polling:
  Continuously poll IOs for change of value
  Pro:
    Simple program, easy to understand
    Events do not block the normal program execuction
  Cons:
    Most polls are unneeded – value did not change
    High CPU usage
    Reaction time depends on #IOs (may be very high)
Interrupt
  Normal execution is interrupted when event occurs
  Pro:
    Processor resources are only used when necessary
  Cons:
    Program execution is interrupted in a non-deterministic manner

## Slide 14: Altera Interrupts
Header files:
#include "altera_avalon_pio_regs.h“
#include "sys/alt_irq.h"

## Slide 15: Altera Interrupts
Initialization
Enable the interrupt for the specific input IOWR_ALTERA_AVALON_PIO_IRQ_MASK(<BASE>, <MASK>);
<BASE> can be e.g. KEY_BASE for buttons
<MASK> specifies the button e.g 0x02 for button 2

## Slide 16: Altera Interrupts
Register handler alt_ic_isr_regsiter(<IRQ_CONTROLLER_ID>, <IRQ>, <isr_function>, <isr_context>, <flags> )
For buttons <IRQ_CONTROLLER_ID> should be KEY_IRQ_INTERRUPT_CONTROLLER_ID
For buttons <IRQ> should be KEY_IRQ
<isr_function> is the callback function (next slide)
<isr_context> are some extra parameters for the function (can bu NULL in our case)
<flags> not needed in our case, set to 0

## Slide 17: Altera Interrupts
Set the edge capability, i.e clear the interrupt
IOWR_ALTERA_AVALON_PIO_EDGE_CAP(<BASE>, <VAL>);
<BASE> same as before
<VAL> should be 1

## Slide 18: Altera Interrupts
Callback function should clear the inerrupt again:
void callback_func(){
IOWR_ALTERA_AVALON_PIO_EDGE_CAP(<BASE>, <VAL>);
//Now handle the actual button press
}
Otherwise the function will be called over and over again!
Now callback_func() will be called when an interrupt happens

## Slide 19: Tasks
Take a look at the template
Fill in the initialize method to set up an interrupt handler for button presses
Create an interrupt handler that reverses the sliding pattern
DO NOT MODIFY main()!
DO NOT USE POLLING!