## Slide 1: Introduction to Pulse Width Modulation (PWM)

## Slide 2: What is PWM
Output signal alternates between on and off within specified period.
Control the power received by a device.
The voltage seen by the load is directly proportional to the source voltage.

## Slide 3: What is PWM?
Depending on the requirement the width of the pulse is modulated (adjusted).
Duty cycle = ton / (ton + toff).
on off
on off
Duty cycle = 20%
Duty cycle = 50%
Width
period
0.2
1
0.5

## Slide 4: Why PWM?
Maximum voltage
100 %
50 %
75 %
Analog voltage control:
  Voltage can be changed to control the motor speed
  Can NIOS change voltage ?
t

## Slide 5: Why PWM?
50 %
Digital voltage control:
  Can only control ‘1’ and ‘0’
  X% of maximum analog voltage = X% of duty cycle
t
t
1
0
Analog control
Digital control
=

## Slide 6: PWM Control Example
Disco gate:
  100 % open gate = 10 persons per second
  50% open gate = 5 persons per second
Analog control:
  Open 50 % gate
  Total how many people can go in 10 seconds?
Digital control:
  Open 100 % gate on every odd second (1,3,5,7,9, ..)
  Total how many people can go in 10 seconds?

## Slide 7: Usage of PWM
Motor Control
Intensity of LED

## Slide 8: How to generate PWM signal ?
Software method
  Using counter
    Count to 100 in a loop
    Set the output value to 1 in the beginning of the loop
    Set the output value to 0 as soon as the counter reaches the value of required duty cycle.
    Continue the process
  Using interrupt
    Home work
    Think about the concept

## Slide 9: Your tasks
Create projects in a usual way using provided SOPCINFO file.
Type the code in your application project.
Change duty cycle variable and observe the effect on oscilloscope or LED.
Using oscilloscope, verify the duty cycle.
  Is it precise?
  Is it efficient?

## Slide 10: Software PWM
Output pin:
  GPIO_0[0]
  Using the manual find out the correct pin and observe the resulting PWM on the oscilloscope
  In C program, use the following instructions to change the output
    IOWR(PIO_0_BASE, 0, 0); // set output 0
    IOWR(PIO_0_BASE, 0, 1); // set output 1
Control LED (optional):
  Apply the PWM signal to LED, observe the intensity

## Slide 11: You are 25 % engineer ALREADY !
Start doing things on your own
Use Google, dictionary to find a solution
Try hard, do not give up to be an expert engineer
I am sure, you all are very hard working and intelligent. You can do the job.
If you have problems call us

## Slide 12: Questions

## Slide 13: Hardware PWM IP
Let us use the NIOS processor as a boss
  Does a boss do work by her/himself?
  The boss only manages/guides/controls the people to do the job
Highest smartness is required in managing people
    Do not think that your boss is an idiot !
    Why the bosses have highest salary world-wide?
Career tip:
  Let only people/machines/tools/computers do your job
  Learn to manage them to get more salary

## Slide 14: Hardware PWM IP
Programmable/configurable
Precise
A good obedient, the boss can RELAX !!!
NIOS core
RAM
JTAG Uart
Your PC
USB Blaster
PWM

## Slide 15: Hardware PWM IP
Follow the simple use sequence
  Enable
  Configure
  Modify
  Disable
Only one function for controlling two PWM signals
motor_setting(phase1, duty1,
phase2, duty2,
period, enable);

## Slide 16: Hardware PWM IP
motor_setting(phase1, duty1,
phase2, duty2,
period, enable);
Enable mask= 1
Disable = 0
Common period

## Slide 17: Questions

## Slide 18: Evaluation Scheme
Give A to the students who finish tasks by implementing C code, IP to generate the pwm wave. The students should also be clear about the difference of C code and hard IP.
Give B who just finish any task.
Give C or D to who cannot do any thing.