## Slide 1: Sensor Data

## Slide 2: 3-axis Accelerometer
an accelerometer at rest on the surface of the earth will measure an acceleration g= 9.81 m/s2 straight upwards, due to its weight

## Slide 3: 3-axis Accelerometer

## Slide 4: 3-axis Gyroscope
A gyroscope is a device for measuring or maintaining orientation, based on the principles of angular momentum, it is to measure the rate of changes of the angles (deg/s)

## Slide 5: 3-axis Gyroscope
Rigidity in space refers to the principle that a wheel with a heavily weighted rim spun rapidly will remain in a fixed position in the plane in which it is spinning.

## Slide 6: 3-axis Gyroscope

## Slide 7: MPU6050
An inertial measurement unit (IMU) is used to measure 3-axis acceleration and 3-axis gyroscope in the unit g and deg/sec. MPU-6050 6-axis motion processor is used for this task. It has I2C bus connection allowing the device to gather data using only two wires, full scale range can be configured from ±2g to ±16g for the accelerometer and ±250°/s to 2000°/s for the gyroscope. The MPU-6050 also uses ADCs for digitizing the accelerometer outputs.

## Slide 8: MPU6050

## Slide 9: Full Scale Range of MPU6050

## Slide 10: Raw Data Processing
The MPU-6050 features ADC that converts analog voltage to a binary number and then to a digital number in base 10 for reading, while analog accelerometers gives voltage level within a predefined range as output that since has to be converted to a digital value using ADC.
The MPU6050 gives 8-bit low and 8-bit high output, combined those bits give 16-bit as output for each of the 6 axis.
A mathematical relationship shows how the numbers of bits an ADC handles. For example, 16-bit output gives a value in the range of 2^16 = 65536 or numbers on the scale 0 to 65535.

## Slide 11: Raw Data Processing
A 16-bit ADC resolution with maximum 3.3V input is:
By dividing the raw accelerometer data by a sensitivity scale factor of 16384 LSB/g for the setting ±2g the data can be converted into multiplies of g.
Dividing the raw gyro data by sensitivity scale factor of 131 LSB/°/s for the setting ± 250°/s gives angular velocity in °/s.

## Slide 12: UART

## Slide 13: UART
Baud：The speed of transmission, for example, 9600 baud = 9600 bits/s,
Which means can transmit 9600 bit per second

## Slide 14: IIC Bus
I2C bus is a multi master bus able to transfer data between two equipment using only two lines, a serial data line and a serial clock line.
When I2C is used to carry information each device is recognized by a unique address.
Vdd
SDA (Serial Data Line)
SCL (Serial Clock Line)
SCLKN1 out
SCLK in
DATA1 out
DATA in
Device

## Slide 15: IIC Bus

## Slide 16: IIC Bus

## Slide 17: Single-axis tilt sensing
where: A = acceleration measured, g = Earth gravity vector

## Slide 18: Dual-axis tilt sensing
Without the help of a third axis (for example the Z axis), it is impossible to distinguish a tilt angle of 30° from one of 150° because the X axis has the same outputs at these two tilt angles

## Slide 19: Tri-axis tilt sensing

## Slide 20: Function：atan2
We use atan2(y,x) instead of atan(y/x) in C programming.

## Slide 21: Using atan2